## Slide 1: Maria’s Restaurant Lesson 20 Appendix B Zone 2 Manual N Loads

## Slide 2
Maria’s Restaurant Design
(Staff: Maria & 7 Employees each shift. Glass Store Front and front door)
66 ft.
25 ft.
F1
R1
S1
DW
C1
CT/O
C2
C3
SP
Fry
R2
F2
Woman’s
Restroom
1 handicap
1 standard
Men’s
Restroom
1 handicap
1 urinal
H1
Bar
Ice
C6
Counter
S3
C7
Bar 12 X 10
Seating 12
Restaurant 33 X 15
11 X 4 & 11 X 6
Seating 58
R3
R4
B1
Shelv.
S2
SK
B = Beverage Area R = Refrigerator (blue walk in
C = Counter S = Sink; S1 Hand; S2 3 Pot; S3 Bar
CT = 4 burner plus flat top over ovens SK= Steam Kettle
DW = Dishwasher SP = Salad/cold Prep table
F = Freezer (blue walk in) H1 = Hot Prep Table with Heat Lamp Shelf
Shelv..
Shelving/Storage
WH
S1
B2

## Slide 3
Maria’s Restaurant Design
(Staff: Maria & 7 Employees each shift. Glass Store Front and front door)
66 ft.
25 ft.
F1
R1
S1
DW
C1
CT/O
C2
C3
SP
Fry
R2
F2
Woman’s
Restroom
1 handicap
1 standard
Men’s
Restroom
1 handicap
1 urinal
H1
Bar
Ice
C6
Counter
S3
C7
Bar 12 X 10
Seating 12
Restaurant 33 X 15
11 X 4 & 11 X 6
Seating 58
R3
R4
B1
Shelv.
S2
SK
B = Beverage Area R = Refrigerator (blue walk in
C = Counter S = Sink; S1 Hand; S2 3 Pot; S3 Bar
CT = 4 burner plus flat top over ovens SK= Steam Kettle
DW = Dishwasher SP = Salad/cold Prep table
F = Freezer (blue walk in) H1 = Hot Prep Table with Heat Lamp Shelf
Shelv..
Shelving/Storage
WH
S1
B2

## Slide 4: Kitchen Area Equipment Cooling Load (Sensible + Latent where applicable)
Refrigeration/Freezer: 3,690 + 3,778 7,468 Btuh
Dish Washer: 4,600 + 6,000 10,600 Btuh
Steam Kettle: 1,280 + 1,280 2,560 Btuh
Two Cook Tops: 16,100 Btuh
Convection Ovens: 11,400 Btuh
Fryers: 3,800 Btuh
Salad Prep Refrigeration: 814 +814 1,628 Btuh
Hot Serve Table: 9,704 + 2,306 12,010 Btuh
Small Appliances: 5,634 +2,120: 7,754 Btuh
Kitchen Equipment Total: 73,320 Btuh
Total Latent Load: 16,298 Btuh

## Slide 5: Restaurant & Bar Area Equipment
For Maria’s Restaurant, the Restaurant and Bar area equipment’s total Btuh value is: 22,186 Btuh
The following section shows how the total Btuh was calculated for each piece of equipment shown on the drawing, and then added to some small appliances and restaurant equipment not shown on the drawing Maria has specified electrical circuits for.

## Slide 6: Zone 2 Speedsheet

## Slide 7: Speedsheet Location Information

## Slide 8: Zone 2 Speedsheet TABS

## Slide 9: Ventilation

## Slide 10: NOTE: ON ERV EFFICIENCY
Manual N abridged edition does not allow the use of two different ventilation values for to reflect the efficiency for the ERV. The values when added are:
An added 3,268 BTUH Total Cooling Load
An added 4,290 BTUH Total Heating Load

## Slide 11: Infiltration

## Slide 12: Ducts

## Slide 13: Internal Loads Lighting & Occupancy

## Slide 14: Internal Loads Equipment
Diversity Factor:
Fraction of active or powered units
For internal gains.

## Slide 15: Floors

## Slide 16: Ceiling

## Slide 17: Walls

## Slide 18: Doors

## Slide 19: Sky Light & Glass

## Slide 20: Database

## Slide 21: N1 Glass

## Slide 22: N1 Doors

## Slide 23: N1 Walls, Ceilings & Floors
Net Areas Needed

## Slide 24: N1 Heating and Cooling Total Loads
Heat Load
Sensible Cooling Load
Total Cooling Load = 93,635 + 18,631 = 112,266 Btuh
Latent Cooling Load

## Slide 25: Zone 2 Manual N Summary

## Slide 26: Field Notes
For many buildings the ducts are located in an unconditioned space. Thus, the Manual N Speedsheet default setting of T, or the actual duct size can be entered to calculate the heat loss/gain. However, to use the Speedsheet for duct inside of the conditioned space, where the ducts have been previously filled in: to remove the #N/A simply change the T or square foot values to 0.